Results and data from Gyöngyösoroszi

# Budapest, 2001

Environmental study of a heavy metal contaminated site situated in

Gyöngyösoroszi, Hungary

## Introduction

Gyöngyösoroszi is a little village in the Mátra in North-Hungary. The former lead and zinc mine has been closed fifteen years ago, but the acidic mine water and the primary and secondary wastes of the mining and the ore processing are still present in open deposits (tailing-dump, precipitate-reservoir), in the sediments of the creek and the lakes and reservoirs on it.

The tailing dump is situated south-east from the village. The volume of the flotation tailing is about 4 millions m3. The southern slope of the tailing dump was covered by a thin (20-40 cm) and discontinuous layer. The thin layer has been inhabited with selected sorts of resistant pioneer plant species. The plants, growing in the thin cover-soil, start the vertical cycling of the toxic metals from the deeper layers up to the surface.

The roughly 50 waste rock heaps have not been assessed or mapped yet, their volume may vary from a few 100 to 10 000 m3 per heap. The heaps differ from each other and are heterogeneous. Rocks contain sulphide-minerals, like galenite or sphalerite. The toxic metal content varies up to a maximum of 100 mg/kg Cd, 0.1% Cu,1% Pb and 3% Zn. During the last 15-30 years bioleaching of the heaps, due to the activity of Thiobacillus has became considerable. Acidity of the surrounding soil may reach pH:2-3. The heaps are washed out by precipitate and temporary water flows.

The main surface water, the Toka creek is situated in the centre of the polluted area. Along the creek there are three reservoirs; the industrial, the agricultural and the Gyöngyösi Lake. The acidic mine water is completely controlled and treated today, but the reservoir of the metal-containing precipitate is not isolated from the environment. The acidic mine water is treated only since about fifteen years. Formerly, the acidic mine outflow was let into the creek and was in situ neutralised with lime in the reservoirs. This huge amount of in situ precipitated toxic metals is still in the sediment of the reservoirs, and floods transport it all over the surface water system and on the surrounding soil. The sediment is disposed on the regularly flooded riverside, on the soil of the hobby gardens.

The soil of the valley is contaminated not only by the sediment but also by the tailing material deriving (erosion, deflation) from the open (not covered) tailing dump. The soils of the grounds close to the Toka creek are used as hobbygardens, also for growing vegetables which have a high bioconcentration capacity. The hobbygardens are long belt-parcels rectangularly oriented to the creek. The contamination of the soil mainly originates from the sediments of the surface waters. In most of the cases the contamination is reduced in the 5-10 m long part of the ground neighbouring to the creek. To lower risk at the site, remediation of the soil is a realistic solution besides or together with changing land use and changing agricultural products, e.g. instead of lettuce and paprika, mostly grapes and berries.

Gyöngyösoroszi is a very good field to examine the impacts of mining activity. Heavy metals are extremely toxic elements, and the deleterious effects on humans are well known. Since the area is not protected against environmental contamination, several sources, exposure pathways and targets are in focus. Therefore the site provides an excellent opportunity for environmental scientists to carry out environmental impact assessment, feasibility studies as well as environmental risk assessment, so many documents already exist. Assessments and surveys were prepared since 1990 by different firms and experts, so the area is partly well known. The sources, the transport routes, exposure routes and target environmental elements and organisms, included humans may be identified and followed on the basis of the present information.

Tailing dump

Tailing material samples from the tailing dump

Burri, P.: Analysis of soil samples from the mining area near Gyöngyösoroszi, 1998.

Sampling date: 1998.07.

| sample | pH | total metal content (mg/kg) | soluble metal content (mg/kg) |
| --- | --- | --- | --- |
|  |  | Zn | Pb | Cu | Zn | Pb | Cu |
| Deep layer, black | 7.0 | 31 858 | 4971 | 2450 | 3.4 | 1.2 | 0.6 |
| Deep layer, red | 7.1 | 2248 | 481 | 114 | 4.3 | 0.1 | 0.0 |
| Deep layer, yellow | 7.3 | 7571 | 2766 | 984 | 3.9 | 1.7 | 0.6 |
| Cover layer | 4.7 | 603 | 186 | 72 | 42.2 | 1.9 | 0.5 |

Heavy metal content of the tailing material on tailing dump

Bekő, J. et al: Gyöngyösoroszi és környéke nehézfém-szennyezettségének vizsgálata, 1992.

Sampling date: 1991.

|  | 3 M | 4 M | 6 M | 8 M |
| --- | --- | --- | --- | --- |
| K w% | 251 | 0 | 0 | 0.964 |
| Ca w% | 5.8 | 7.2 | 19.8 | 4.9 |
| Ti ppm | 0 | 3590 | 0 | 0 |
| Cr ppm | 1680 | 1450 | 0 | 90 |
| Mn ppm | 2670 | 3870 | 51060 | 821 |
| Fe w% | 11.0 | 17.2 | 16.0 | 1.8 |
| Co ppm | 606 | 0 | 0 | 175 |
| Cu ppm | 5940 | 6140 | 0 | 1010 |
| Zn w% | 9.1 | 11.3 | 22.1 | 1.9 |
| As ppm | 0 | 0 | 84 | 0 |
| Rb ppm | 16 | 0 | 5 | 134 |
| Sr ppm | 297 | 278 | 205 | 166 |
| Y ppm | 0 | 74 | 18 | 0 |
| Zr ppm | 267 | 264 | 1 | 110 |
| Nb ppm | 5 | 0 | 3 | 3 |
| Mo ppm | 66 | 43 | 23 | 12 |
| Cd ppm | 6 | 0 | 66 | 46 |
| Pb ppm | 7041 | 21120 | 53 | 2970 |

Sampling sites:

3M	grey tailing material next to Felső tó

4M	light grey tailing material next to 3M

6M	tailing material next to the drain tube under the tailing dump

8M	north bank of Középső tó

Heavy metal content of the water samples from the lake on tailing dump

Bekő, J. et al: Gyöngyösoroszi és környéke nehézfém-szennyezettségének vizsgálata, 1992.

Sampling date: 1991.

| Water | pH | Zn | Pb | Cd |
| --- | --- | --- | --- | --- |
| Felső tó 1 | 7.37 | 0.50 ppm | 60.00 ppb | 50.00 ppb |
| Felső tó 2 | 7.57 | 0.73 ppm | 41.00 ppb | 84.00 ppb |
| Alsó tó 2 | 4.40 | 3.40 ppm | 0.16 ppm | 32.00 ppb |
| Alsó tó 4 | 4.36 | 3.65 ppm | 0.16 ppm | 47.00 ppb |

# Heavy metal content of selected plants from the tailing dump

Brombacher, C., Guadagnini M.: Heavy metal content of selected plants from a former mining area near Gyöngyösoroszi, Hungary, 1998.

Sampling date: 1998.07.

| species | location | Zn (mg/kg dry wet) | Cu (mg/kg dry wet) | Cd (mg/kg dry wet) |
| --- | --- | --- | --- | --- |
| Achillea millefolium | n.d. | 255,4 | 17,0 | 2,38 |
| Agrostis sp. | north west | 409,8 | 31,9 | 6,26 |
| Carex sp. | north west | 354,6 | 55,0 | 3,01 |
| Echium vulgare | north west | 607,5 | 45,3 | 4,96 |
| Equisetum palustre | n.d. | 754,5 | 7,9 | 0,73 |
| Phalaris canadiensis | n.d. | 144,9 | 4,1 | 0,51 |
| Phragmites australis | north west | 767,5 | 40,5 | 0,70 |
| Populus sp. | north west | 1158,5 | 12,9 | 19,5 |
| Robinia pseudoacacia | n.d. | 159,8 | 13,3 | 0,91 |
| Robinia pseudoacacia | top | 212,7 | 9,0 | 0,65 |
| Silene alba | north west | 693,5 | 50,4 | 2,6 |
| Silene vulgaris (cucubulus) | north west | 505,5 | 20,7 | 4,55 |
| Solamum dolcamare | north west | 31,8 | 52,0 | 10,7 |
| Tussilago falifara | north west | 568,5 | 38,9 | 8,75 |

Water results along the Toka creek

Bekő, J. et al: Gyöngyösoroszi és környéke nehézfém-szennyezettségének vizsgálata, 1992.

Sampling date: 1991.

| sampling sites | pH | Zn concentration | Pb concentration | Cd concentration |
| --- | --- | --- | --- | --- |
| 2 | 4,9 | 0,44 ppm | 6,60 ppb | 3,00 ppb |
| 2é | 2,6 | 7,00 ppm | 55,00 ppb | 24,00 ppb |
| 4a | 4,9 | 0,41 ppm | 14,00 ppb | 3,00 ppb |
| 4b | 6,2 | 2,80 ppm | 7,50 ppb | 16,50 ppb |
| 6 | 7,37 | 0,44 ppm | 3,00 ppb | 6,00 ppb |
| 7 | 7,51 | 0,10 ppm | 18,00 ppb | <<5 ppb |
| 8 | 7,45 | 0,60 ppm | 18,00 ppm | <<5 ppb |
| 10 | 7,71 | 0,24 ppm | 29,00 ppb | <<5 ppb |
| 12 | 7,85 | 0,45 ppm | 16,00 ppb | <<5 ppb |
| 13 | 7,87 | 0,50 ppm | 13,60 ppb | <<5 ppb |
| 14 | 7,93 | 0,97 ppm | 15,00 ppb | <<5 ppb |
| 20 | 7,77 | 0,40 ppm | 9,90 ppb | <<5 ppb |
| agricultural reservoir 1 | 8,14 | 0,15 ppm | 6,00 ppb | <<5 ppb |
| agricultural reservoir 2 | 7,64 | 90,00 ppb | 4,60 ppb | <<5 ppb |
| agricultural reservoir 3 | 8,09 | 7,00 ppb | 20,00 ppb | 12,00 ppb |
| between the agricultural reservoir and Gyöngyösi lake | 7,89 | 0,25 ppm | 5,00 ppb | <<5 ppb |
| Gyöngyösi lake 1 | 7,95 | 0,38 ppm | 9,30 ppb | 4,30 ppb |
| Gyöngyösi lake 2 | 7,52 | 0,18 ppm | 7,00 ppb | <<5 ppb |
| Gyöngyösi lake 3 | 8,13 | 2,70 ppb | 19,00 ppb | 19,00 ppb |

Sampling sites:

2	under the former pithead

2é	under with 50 meter from 2

4a	clearness mine inflow which running from adit

4b	water neutralisation plant

6	before the bridge

7	under the industrial reservoir

- before the bridge

10	after the bridge

- after shallow water

13	opposite to the Kossuth street 22

14	opposite to the Petőfi street 1-4

20	inflow of Toka-creek to the agricultural reservoir

Sediment of surface water

Sediment results along the Toka creek

North-Hungarian Environmental Authority: Survey on the sediment of Toka-valley, Miskolc, Hungary, 1996

Sampling date: 1996.10.

|  | Pb (mg/kg) | Zn (mg/kg) | Cd (mg/kg) | Cr (mg/kg) | Cu (mg/kg) | As (mg/kg) | pH | ( ((S/cm) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Upstream of the mine | 110 | 420 | 0,99 | 9,63 | 43,4 | 60,9 | 5,95 | 760 |
| After the water neutralisation plant | 113 | 5560 | 19,7 | 8,18 | 121 | 89,4 | 7,52 | 1500 |
| After the industrial reservoir | 1568 | 4190 | 18,8 | 24,8 | 345 | 162 | 7,55 | 1520 |
| Before Gyöngyösoroszi | 484 | 2410 | 7,69 | 17,6 | 112 | 146 | 7,1 | 1600 |
| After Gyöngyösoroszi at the bridge | 518 | 2320 | 8,29 | 26,4 | 141 | 100 | 7,55 | 1650 |
| After the agricultural reservoir | 49,1 | 1740 | 3,54 | 33,7 | 67,8 | 54,7 | 7,66 | 1270 |

Sediment results of the reservoirs

North-Hungarian Environmental Authority: Survey on the sediment of Toka-valley, Miskolc, Hungary, 1996

Sampling date: 1996.10.

|  | Pb (mg/kg) | Zn (mg/kg) | Cd (mg/kg) | Cr (mg/kg) | As (mg/kg) | Cu (mg/kg) |
| --- | --- | --- | --- | --- | --- | --- |
| Industrial reservoir, average | 273 | 17500 | 186,1 | 11,98 | 475,91 | 223,83 |
| Limit value transgression (average/Holland limit value) | 3,2* | 125* | 233* | 0,12* | 16,4* | 6,2* |
| Industrial reservoir, maximum | 497 | 145200 | 564 | 13,3 | 1275 | 949 |
| Agricultural reservoir, average | 739,93 | 2957,3 | 14,56 | 26,58 | 97,6 | 162,5 |
| Limit value transgression (average/Holland limit value) | 8,7* | 21,2* | 18,2* | 0,26* | 3,4* | 4,5* |
| Agricultural reservoir, maximum | 997 | 4230 | 20,1 | 30,6 | 137 | 190 |

Sediment results of the reservoirs

North-Hungarian Environmental Authority: Survey on the sediment of Toka-valley, Miskolc, Hungary, 1996

Sampling date: 1996.10.

Industrial reservoir			Industrial reservoir			Industrial reservoir

Cadmium (mg/kg)			    Lead (mg/kg)			     Zinc (mg/kg)

#### Agricultural reservoir		           Agricultural reservoir		          Agricultural reservoir

Cadmium (mg/kg)		                   Lead (mg/kg)		                 Zinc (mg/kg)

Macroinvertebrates in the Toka creek

Sipter, E.: A Trent-index alkalmazhatóságának bemutatása, 1999.

Sampling date: 1998.07.

| Species | Sampling sites |
| --- | --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 |
| EPHEMEROPTERA |  |  |  |  |  |  |
| Baetis sp. | + | + | + | + | + | + |
| Ecdyonorus quadrilineatus |  |  |  |  |  |  |
| Epeorus silvicola |  |  |  |  |  |  |
| Ecdyonurus venosus |  |  |  |  |  |  |
| Paraleptophlebia submarginata |  |  |  |  |  |  |
| Ephemera danica |  |  |  |  |  |  |
| Heptagenia sp. | + |  |  |  |  | + |
| PLECOPTERA |  |  |  |  |  |  |
| Capnia sp. |  |  |  |  |  |  |
| Leuctra sp. |  |  |  |  |  |  |
| TRICHOPTERA |  |  |  |  |  |  |
| Hydropsychidae | + |  |  | + | + | + |
| Chetopteryx sp. |  |  |  |  |  |  |
| Rhyacophila sp. | + |  |  | + | + | + |
| AMPHIPODA |  |  |  |  |  |  |
| Gammaridae |  |  |  | + |  |  |
| ISOPODA |  |  |  |  |  |  |
| Asellus aquaticus |  |  |  |  |  |  |
| ODONATA |  |  |  |  |  |  |
| Platicnemis pennipes |  |  |  |  |  | + |
| Agrion virgo | + | + | + |  |  |  |
| Agrion splendens |  |  |  |  |  |  |
| PHARYNGOBDELLIDEA |  |  |  |  |  |  |
| Erpobdella octoculata |  |  |  |  |  |  |
| Dina linneata |  |  |  |  |  |  |
| DIPTERA |  |  |  |  |  |  |
| Chironomidae | + |  |  |  | + | + |
| Tabanidae |  |  |  |  |  | + |
| NEUROPTERA |  |  |  |  |  |  |
| Sialis sp. |  |  |  |  |  |  |

+: 1 or more in the sample

Sampling sites:

1	Upstream of the mine

- After the water neutralisation plant

- After the industrial reservoir

- Before Gyöngyösoroszi

- After Gyöngyösoroszi at the bridge

- After the agricultural reservoir

# Soil and plant results from hobbygardens along the Toka-creek

# Result of soil samples from Gyöngyös, next to Toka creek

National Health and Medical Service: Report about the soil and plant chemistry test on periphery of Gyöngyös and Gyöngyösoroszi, 1991.

Sampling date: 1991.

| sample number | topographical number | name of the owner | distance from the creek (m) | Pb (mg/kg) | Cd (mg/kg) |
| --- | --- | --- | --- | --- | --- |
| 19 | 5274/4 | Vályi Nagy Károly | 5 | 295.1 | 2.50 |
| 20 | 5274/4 | Vályi Nagy Károly | 10 | 772.8 | 4.80 |
| 21 | 5274/4 | Vályi Nagy Károly | 20 | 112.5 | 0.55 |
| 22 | 5274/4 | Vályi Nagy Károly | 30 | 27.1 | 0.20 |
| 23 | 5274/4 | Vályi Nagy Károly | 50 | 42.2 | 0.28 |
| 24 | 5274/4 | Vályi Nagy Károly | 60 | 25.8 | 0.16 |

# Result of soil samples from Gyöngyösoroszi, next to Toka creek

National Health and Medical Service, Report about the soil and plant chemistry test on periphery of Gyöngyös and Gyöngyösoroszi, 1991.

Sampling date: 1991.

| sample number | topographical number | name of the owner | distance from the creek (m) | Pb (mg/kg) | Cd (mg/kg) |
| --- | --- | --- | --- | --- | --- |
| 76 |  | Tóth Tiborné | 15 | 28.6 | 0.12 |
| 77 |  | Tóth Tiborné | 5 | 387.8 | 2.20 |
| 78 |  | Tóth Tiborné | 10 | 308.3 | 10.90 |
| 79 |  | Tóth Tiborné | 15 | 30.8 | 0.13 |
| 80 |  | Tóth Tiborné | 5 | 25.6 | 0.20 |

# Soil results from the hobbygardens

North-Hungarian Environmental Authority: Survey on the sediment of Toka-valley, Miskolc, Hungary, 1996

Sampling date: 1996.10.

|  | Pb (mg/kg) | Zn (mg/kg) | Cd (mg/kg) | Cr (mg/kg) | As (mg/kg) | Cu (mg/kg) |
| --- | --- | --- | --- | --- | --- | --- |
| Hobbygardens in the village, average | 265,5 | 1066 | 3,44 | 10,3 | 123,69 | 105,1 |
| Limit value transgression (average/limit value) | 3,1* | 7,6* | 4,3* | 0,1* | 4,2* | 2,9* |
| Hobbygardens in the village, maximum | 853 | 2730 | 9,75 | 15,3 | 262 | 225 |
| Hobbygardens after the village, average | 613,7 | 2487 | 12,45 | 20,06 | 196,6 | 156,6 |
| Limit value transgression (average/limit value) | 7,2* | 17,8* | 15,6* | 0,2* | 6,8* | 4,5* |
| Hobbygardens after the village, maximum | 900 | 3650 | 23,4 | 23,7 | 405 | 308 |

### Results of plant samples from Gyöngyös

National Health and Medical Service: Report about the soil and plant chemistry test on periphery of Gyöngyös and Gyöngyösoroszi, 1991.

Sampling date: 1991.

| sample number | topographical number | name of the owner | plant species | Pb (mg/kg) | Cd (mg/kg) |
| --- | --- | --- | --- | --- | --- |
| 164 | 5274/4 | Vályi Nagy Károly | lettuce | 0.13 | 0.01 |
| 165 | 5274/4 | Vályi Nagy Károly | rhubarb | 0.05 | 0.06 |
| 166 | 5274/4 | Vályi Nagy Károly | horseradish | 0.06 | 0.07 |
| 167 | 5274/4 | Vályi Nagy Károly | chives | 0.07 | 0.06 |
| 168 | 5274/4 | Vályi Nagy Károly | gooseberry | 0.03 | 0.01 |
| 172 | 5274/4 | Vályi Nagy Károly | sorrel | 0.04 | 0.01 |
| 242 | 5274/4 | Vályi Nagy Károly | strawberry | <0.01 | <0.01 |
| 243 | 5274/4 | Vályi Nagy Károly | red currant | n.d. | <0.01 |
| 244 | 5274/4 | Vályi Nagy Károly | kohlrabi | <0.01 | <0.01 |
| 265 | 5274/4 | Vályi Nagy Károly | raspberry | <0.01 | 0.01 |
| 327 | 5274/4 | Vályi Nagy Károly | string beans | <0.01 | <0.01 |
| 328 | 5274/4 | Vályi Nagy Károly | apple | <0.01 | <0.01 |
| 329 | 5274/4 | Vályi Nagy Károly | pear | <0.01 | <0.01 |
| 330 | 5274/4 | Vályi Nagy Károly | tomato | <0.01 | <0.01 |

Average BCF of plants from hobbygardens along the Toka creek

Bekő, J. et al: Gyöngyösoroszi és környéke nehézfém-szennyezettségének vizsgálata, 1992.

Sampling date: 1991.

|  | onion | horseradish | spring bean | sorrel | potato | rhubarb |
| --- | --- | --- | --- | --- | --- | --- |
| As | 0.005 | 0.005 | 0.05 | n.d. | n.d. | n.d. |
| Cd | 5 | 25 | 5 | 50 | 10 | 25 |
| Cu | 5 | 15 | 15 | 10 | n.d. | 5 |
| Pb | 1 | 1 | 1 | 1 | 0.5 | 1 |
| Zn | 1 | 50 | 10 | 15 | n.d. | 10 |

|  | kohlrabi | tomato | rye- grass | horseshoe | plum | beetroot |
| --- | --- | --- | --- | --- | --- | --- |
| As | n.d. | n.d. | 0.05 | 0.1 | n.d. | n.d. |
| Cd | 5 | 1 | n.d. | n.d. | 5 | 5 |
| Cu | 25 | 5 | n.d. | n.d. | 15 | 15 |
| Pb | 1 | 0.5 | n.d. | n.d. | 0.5 | 1 |
| Zn | 10 | 10 | 0.1 | 0.1 | 5 | 50 |

| metals | red currant | raspberry | gooseberry | melon | grape | garlic |
| --- | --- | --- | --- | --- | --- | --- |
| As | n.d. | n.d. | n.d. | n.d. | n.d. | n.d. |
| Cd | 5 | 10 | 5 | 1 | 0.5 | 50 |
| Cu | 5 | 10 | 5 | n.d. | n.d. | n.d. |
| Pb | 1 | 1 | 1 | 0.5 | 0.5 | 0.5 |
| Zn | 1 | 1 | 5 | n.d. | n.d. | n.d. |

|  | marrow | peach | lettuce | apple | pear | strawberry |
| --- | --- | --- | --- | --- | --- | --- |
| As | n.d. | n.d. | n.d. | n.d. | n.d. | n.d. |
| Cd | 1 | 1 | 25 | 1 | 1 | 25 |
| Cu | 1 | 5 | 15 | 5 | 15 | 5 |
| Pb | 0.5 | 0.5 | 2 | 1 | 1 | 1 |
| Zn | 1 | 5 | 10 | 0.5 | 5 | 5 |

|  | maize | watermelon | green peas | parsnip | leaf of turnip | turnip |
| --- | --- | --- | --- | --- | --- | --- |
| As | n.d. | n.d. | n.d. | n.d. | n.d. | n.d. |
| Cd | 5 | 1 | 1 | 50 | 25 | n.d. |
| Cu | n.d. | n.d. | n.d. | n.d. | 1 | 1 |
| Pb | 1 | 1 | 1 | 0.5 | 0.1 | 0.01 |
| Zn | n.d. | n.d. | n.d. | n.d. | 1 | 0.5 |

|  | leaf of carrot | carrot | radish | leaf of radish | shaft of radish | root of radish |
| --- | --- | --- | --- | --- | --- | --- |
| As | n.d. | n.d. | n.d. | n.d. | n.d. | n.d. |
| Cd | 50 | n.d. | n.d. | n.d. | n.d. | n.d. |
| Cu | 1 | 1 | n.d. | 0.05 | n.d. | 1 |
| Pb | n.d. | n.d. | 0.5 | n.d. | n.d. | n.d. |
| Zn | 0.5 | 0.5 | n.d. | 0.05 | 0.05 | 0.1 |